CLEAN: Iterative Deconvolution
Fundamentals of Radio Interferometry (Chapter 6)
Griffin Foster
SKA SA/Rhodes University
NASSP 2016

---
Sky Model Convolved with Array PSF
Sky Model
KAT-7 PSF

---
Sky Model Convolved with Array PSF
PSF Convolved with Sky Model
Dirty Image
Difference

---
How do we separate out the signal (the sky model) from the noise?

---
Naïve Deconvolution: Inverse Filtering
Given a function h with is the convolution of two other functions g and f:
Given, h and one of the other functions, say g then f can be deconvolved by using the convolution theorem:
This is called inverse filtering
h = f \circ g
f = \mathcal{F}^{-1} \{\mathcal{F}\{f\}\} = \mathcal{F}^{-1} \left \{ \frac{\mathcal{F}\{h\}}{\mathcal{F}\{g\}} \right \}

---
Naïve Deconvolution: Inverse Filtering
Our deconvolution problem is to recover the true sky image from the PSF and the dirty image
We can try to recover the true sky image with this method:
Unfortunately...
I_{true} = \mathcal{F}^{-1} \left \{ \frac{\mathcal{F}\{I^D\}}{\mathcal{F}\{\textrm{PSF}\}} \right \}
I^D = \text{PSF} \circ I_{true}

---
Naïve Deconvolution: Inverse Filtering
Sky Model Recovered Using Inverse Filtering
True Sky Model

---
Naïve Deconvolution: Inverse Filtering
Inverse filtering only works when there is NO noise in the measurement. Unfortunately, there is noise in any real world measurement.
Sky noise, instrumentational noise, computation error...
I^D = \text{PSF} \circ I_{true} + \epsilon

---
Naïve Deconvolution: Thresholding
Sky Model Recovered Using Thresholding
Thresholded Dirty Image

---
Sky Model using Point Source Components
Fourier transform of a Dirac delta-function, by the Fourier shift theorem, is a simple complex phase function and the constant flux
= C(\nu) \cdot e^{-2 \pi i (ul_0 + vm_0)}
\mathscr{F} \{ C(\nu) \cdot \delta\,(l- l_0, m - m_0)\}(u, v) =
C(\nu) \cdot\iint \limits_{-\infty}^{\infty} \delta\,(l- l_0, m - m_0) \, e^{-2 \pi i (ul + vm)}\,dl\,dm

---
Sky Model using Point Source Components
Source ID	RA (Hours)	Dec (degrees)	Flux (Jy)	Spectral Index
1	00:02:18.81	-29:47:17.82	3.55	-0.73
2	00:01:01.84	-30:06:27.53	2.29	-0.52
3	00:03:05.54	-30:00:22.57	1.01	-0.60
...	...	...	...	...
N	00:02:17.01	-30:01:34.57	0.001	-0.71
To compute model visibilities for deconvolution and self-calibration (in a few weeks) we want to use functions which have an analytic Fourier form (delta functions, Gaussian) to reduce computation time.

---
Resolved Sources
A point source will have the same flux at any baseline length. Any resolved source will have a baseline length dependent flux response.

---
Results of Deconvolution
Residual Image
Restored Image

---
CLEAN: A Simple Example
True Sky Model (with Noise)
Point Spread Function

---
CLEAN: A Simple Example
True Sky Model (with Noise)
Point Spread Function
Dirty Image

---
CLEAN: A Simple Example
Högbom's Algorithm (Image-domain CLEAN):
1. Make a copy the dirty image ID(l,m) called the residual image IR(l,m).
2. Find the maximum pixel value and position of the maximum in the residual image IR(l,m).
3. Subtract the PSF multiplied by the peak pixel value fmax and a gain factor g from the residual image IR(l,m) at the position of the peak.
4. Record the position and magnitude of the point source subtracted in a model, i.e. g fmax.
5. Go to (Step 2.), unless all remaining pixel values are below some user-specified threshold or the number of iterations have reached some user-specified limit.
6. Convolve the accumulated point source sky model with a restoring beam, termed the CLEAN beam (usually a 2-D Gaussian fit to the main lobe of the PSF)
7. Add the remainder of the residual image IR(l,m) to the CLEAN image formed in (6.) to form the final restored image.
Input: Dirty image, PSF
Parameters: gain, iteration limit OR flux threshold
Output: Sky model, residual image, restored image

---
CLEAN: A Simple Example
Dirty Image
Residual Image

---
CLEAN: A Simple Example
Dirty Image
Residual Image

---
CLEAN: A Simple Example
Clean components:
   x y flux
32 15 0.273542117836
32 15 0.218833694269
30 34 0.197043506304
32 15 0.175066955415
20 20 0.164478127268
30 34 0.157634805043
31 14 0.141743159144
20 21 0.133470733705
30 34 0.126107844035
32 20 0.124271249713
31 14 0.113394527315
29 18 0.113236796988
19 20 0.11300001035
31 16 0.109407177869
38 21 0.109218346103
21 19 0.109080307468
25 25 0.106739789818
32 9 0.106513135995
30 34 0.100886275228
Same position, different amount of flux. The final sky model is the sum of the different components at the same position

---
CLEAN: A Simple Example
True Sky Model
Deconvolved Sky Model

---
CLEAN: A Simple Example
Point Spread Function
PSF Main Lobe

---
CLEAN: A Simple Example
Restoring Beam/ Restoring PSF

---
True Sky Model
Dirty Image
Deconvolved Sky Model
Restored Image

---
CLEAN: KAT-7 Example
Dirty Image
Restored Image

---
CLEAN: Högbom's Method (Image-domain)
\textbf{input: } I^{D}(l,m), \ \textrm{PSF}(l,m), \ \gamma, \ f_{\textrm{thresh}}, \ N
\textbf{initialize: } S^{\textrm{model}} \leftarrow \{\}, I^{\textrm{res}} \leftarrow I^{D}, i \leftarrow 0
\textbf{while} \ \textrm{any}(I^{\textrm{res}} > f_{\textrm{thresh}}) \ \textrm{or} \ i \leq N \ \textbf{do:}
f_{\textrm{max}} \leftarrow I^{D}(l_{\textrm{max}}, m_{\textrm{max}})
I^{\textrm{res}} \leftarrow I^{\textrm{res}} - \gamma \cdot f_{\textrm{max}} \cdot \textrm{PSF}(l+l_{\textrm{max}}, m+m_{\textrm{max}})
S^{\textrm{model}} \leftarrow S^{\textrm{model}} + \{l_{\textrm{max}}, m_{\textrm{max}}: \gamma \cdot f_{\textrm{max}}\}
i \leftarrow i +1
\textbf{ouput: } S^{\textrm{model}}, I^{\textrm{res}}
l_{\textrm{max}}, m_{\textrm{max}} \leftarrow \underset{l,m}{\operatorname{argmax}} \, I^{\textrm{res}}(l,m)

---
CLEAN: Input Parameters
Point Spread Function Image (real, positive valued N x N array)
Dirty Image (real, positive valued N x N array)
: gain factor, between 0 and 1, determines the rate of deconvolution. Typically set around 0.1
: flux threshold stopping criteria, once the maximum flux is at this level then halt.
: maximum number of iterations to preform.
\textbf{input: } I^{D}(l,m), \ \textrm{PSF}(l,m), \ \gamma, \ f_{\textrm{thresh}}, \ N
\gamma
f_{\textrm{thresh}}
N

---
CLEAN: Initialization and Output
: empty delta-function sky model
: initialize the initial residual image to be the dirty image
: set iteration counter to zero
: final sky model of delta-function components
: residual noise not deconvolved
: (optional) sky model restored image with the ideal PSF
\textbf{initialize: } S^{\textrm{model}} \leftarrow \{\}, I^{\textrm{res}} \leftarrow I^{D}, i \leftarrow 0
\textbf{ouput: } S^{\textrm{model}}, I^{\textrm{res}}
S^{\textrm{model}}
I^{\textrm{res}}
i
S^{\textrm{model}}
I^{\textrm{res}}
I^{\textrm{restored}}

---
CLEAN: Iterative Loop
Subtract the PSF image from the position of the peak flux, attenuated by the gain factor to update the residual image.
Add the flux and position of the component subtracted from the residual image.
I^{\textrm{res}} \leftarrow I^{\textrm{res}} - \gamma \cdot f_{\textrm{max}} \cdot \textrm{PSF}(l+l_{\textrm{max}}, m+m_{\textrm{max}})
S^{\textrm{model}} \leftarrow S^{\textrm{model}} + \{l_{\textrm{max}}, m_{\textrm{max}}: \gamma \cdot f_{\textrm{max}}\}

---
CLEAN: Clark's Method (Gridded Visibility-domain)
\textbf{initialize: } S^{\textrm{model}} \leftarrow \{\}, \ I^{\textrm{res}} \leftarrow I^{D}, \ i \leftarrow 0, \ (\textrm{PSF}_{\textrm{sub}}(l,m), \ R_{\textrm{PSF}}) \leftarrow g(\textrm{PSF}(l,m))
\textbf{input: } I^{D}(l,m), \ \textrm{PSF}(l,m), \ \gamma, \ f_{\textrm{thresh}}, \ N
\textbf{while} \ \textrm{any}(I^{\textrm{res}} > f_{\textrm{thresh}}) \ \textrm{or} \ i \leq N \ \textbf{do:} \quad [\textrm{Major Cycle}]
l_{\textrm{max}}, m_{\textrm{max}} \leftarrow \underset{l,m}{\operatorname{argmax}} \, I^{\textrm{res}}(l,m)
f_{\textrm{max}} \leftarrow I^{D}(l_{\textrm{max}}, m_{\textrm{max}})
S^{\textrm{model}}_{\textrm{partial}} \leftarrow \textrm{Hogbom}(I^{\textrm{res}}, \ \textrm{PSF}_{\textrm{sub}}, \ \gamma, \ f_{\textrm{max}} \cdot R_{\textrm{PSF}}) \quad [\textrm{Minor Cycle}]
S^{\textrm{model}} \leftarrow S^{\textrm{model}} + S^{\textrm{model}}_{\textrm{partial}}
i \leftarrow i +1
\textbf{ouput: } S^{\textrm{model}}, I^{\textrm{res}}
V^{\textrm{model}}_{\textrm{partial}} \leftarrow \mathcal{F}\{S^{\textrm{model}}_{\textrm{partial}}\}, V^S \leftarrow \mathcal{F}\{\textrm{PSF}\}
I^{\textrm{res}} \leftarrow I^{\textrm{res}} - \mathcal{F}^{-1}\{V^S \cdot V^{\textrm{model}}_{\textrm{partial}}\}

---
CLEAN: Clark's Method (Gridded Visibility-domain)
Same Inputs as Högbom's Method
\textbf{initialize: } S^{\textrm{model}} \leftarrow \{\}, \ I^{\textrm{res}} \leftarrow I^{D}, \ i \leftarrow 0, \ (\textrm{PSF}_{\textrm{sub}}(l,m), \ R_{\textrm{PSF}}) \leftarrow g(\textrm{PSF}(l,m))
\textbf{input: } I^{D}(l,m), \ \textrm{PSF}(l,m), \ \gamma, \ f_{\textrm{thresh}}, \ N
\textbf{while} \ \textrm{any}(I^{\textrm{res}} > f_{\textrm{thresh}}) \ \textrm{or} \ i \leq N \ \textbf{do:} \quad [\textrm{Major Cycle}]
l_{\textrm{max}}, m_{\textrm{max}} \leftarrow \underset{l,m}{\operatorname{argmax}} \, I^{\textrm{res}}(l,m)
f_{\textrm{max}} \leftarrow I^{D}(l_{\textrm{max}}, m_{\textrm{max}})
S^{\textrm{model}}_{\textrm{partial}} \leftarrow \textrm{Hogbom}(I^{\textrm{res}}, \ \textrm{PSF}_{\textrm{sub}}, \ \gamma, \ f_{\textrm{max}} \cdot R_{\textrm{PSF}}) \quad [\textrm{Minor Cycle}]
S^{\textrm{model}} \leftarrow S^{\textrm{model}} + S^{\textrm{model}}_{\textrm{partial}}
i \leftarrow i +1
\textbf{ouput: } S^{\textrm{model}}, I^{\textrm{res}}
V^{\textrm{model}}_{\textrm{partial}} \leftarrow \mathcal{F}\{S^{\textrm{model}}_{\textrm{partial}}\}, V^S \leftarrow \mathcal{F}\{\textrm{PSF}\}
I^{\textrm{res}} \leftarrow I^{\textrm{res}} - \mathcal{F}^{-1}\{V^S \cdot V^{\textrm{model}}_{\textrm{partial}}\}

---
CLEAN: Initialization
A function which selects a subset of the PSF and reports the highest PSF sidelobes.
Most of the power in the PSF is centred around the main lobe → we only need a subset of the PSF
For the minor cycle we do a shallow deconvolution down to the level of the highest sidelobe.
\textbf{initialize: } S^{\textrm{model}} \leftarrow \{\}, \ I^{\textrm{res}} \leftarrow I^{D}, \ i \leftarrow 0, \ (\textrm{PSF}_{\textrm{sub}}(l,m), \ R_{\textrm{PSF}}) \leftarrow g(\textrm{PSF}(l,m))

---
CLEAN: Minor Cycle
The minor cycle is a shallow cycle of Högbom's method to a flux threshold determined by the highest PSF sidelobes to produce a partial sky model.
S^{\textrm{model}}_{\textrm{partial}} \leftarrow \textrm{Hogbom}(I^{\textrm{res}}, \ \textrm{PSF}_{\textrm{sub}}, \ \gamma, \ f_{\textrm{max}} \cdot R_{\textrm{PSF}})
l_{\textrm{max}}, m_{\textrm{max}} \leftarrow \underset{l,m}{\operatorname{argmax}} \, I^{\textrm{res}}(l,m)
f_{\textrm{max}} \leftarrow I^{D}(l_{\textrm{max}}, m_{\textrm{max}})

---
CLEAN: Major Cycle
After the minor cycle, Fourier transform the partial sky model into visibilities, combine with the visibility sampling function and produce a partial sky model image.
Subtract the partial sky model image from the residual image, update full sky model with partial sky model.
\textbf{while} \ \textrm{any}(I^{\textrm{res}} > f_{\textrm{thresh}}) \ \textrm{or} \ i \leq N \ \textbf{do:}
\textrm{MINOR CYCLE}
V^{\textrm{model}}_{\textrm{partial}} \leftarrow \mathcal{F}\{S^{\textrm{model}}_{\textrm{partial}}\}, V^S \leftarrow \mathcal{F}\{\textrm{PSF}\}
I^{\textrm{res}} \leftarrow I^{\textrm{res}} - \mathcal{F}^{-1}\{V^S \cdot V^{\textrm{model}}_{\textrm{partial}}\}
S^{\textrm{model}} \leftarrow S^{\textrm{model}} + S^{\textrm{model}}_{\textrm{partial}}

---
CLEAN: Cotton-Schwab's Method (Visibility-domain)
Standard method which is implemented in most modern deconvolving imagers.
Requires the use of gridder/de-gridder functions, computationally more expensive but produces more accurate results.
Ungridded Visibilities
S^{\textrm{model}} \leftarrow S^{\textrm{model}} + S^{\textrm{model}}_{\textrm{partial}}
\mathcal{V}^{\textrm{model}}_{\textrm{partial}} \leftarrow \textrm{degrid}(\mathcal{F}\{S^{\textrm{model}}_{\textrm{partial}}\})
\mathcal{V}^{\textrm{residual}} \leftarrow \mathcal{V}^{\textrm{residual}} - \mathcal{V}^{\textrm{model}}_{\textrm{partial}}
V^{\textrm{residual}} \leftarrow \textrm{grid}(\mathcal{V}^{\textrm{residual}})
I^{\textrm{residual}} \leftarrow \mathcal{F}^{-1}\{V^{\textrm{residual}}\}

---
Method Comparison
Högbom (image-domain):
- pro: easy to implement
- con: limited accuracy in PSF subtraction (e.g w-term effects)
- con: can not account for aliasing artefacts
Clark (gridded visibility-domain):
- pro: only minimally more effort to implement compared to Högbom
- pro: improved aliasing response
- con: limited accuracy in PSF subtraction (e.g w-term effects)
Cotton-Schwab (visibility-domain):
- pro: accurate subtraction of sky model, we can include beam and w-term effects
- con: computationally expensive

---
Method Comparison
Short version:
Högbom and Clark methods are easy to implement (the next assignment is to implement a portion of Clark's method).
But, in almost all cases you should use the Cotton-Schwab method as computation costs are not really to much of a problem these days.

---
Idealized Synthesis Telescope Image
Restored Image
{\color{white}I_{\textrm{restored}} = I_{\textrm{skymodel}} \circ \textrm{PSF}_{\textrm{ideal}} + I_{\textrm{residual}}}

---
CLEAN: KAT-7 Example
Residual Image
Sky Model
Niterations = 0

---
CLEAN: KAT-7 Example
Residual Image
Sky Model
Niterations = 1

---
CLEAN: KAT-7 Example
Residual Image
Sky Model
Niterations = 10

---
CLEAN: KAT-7 Example
Residual Image
Sky Model
Niterations = 100

---
CLEAN: KAT-7 Example
Residual Image
Sky Model
Niterations = 300

---
CLEAN: Filling in the Visibility Space
Restored Image
Restored Visibilities
Niterations = 3

---
CLEAN: Filling in the Visibility Space
Restored Image
Restored Visibilities
Niterations = 30

---
CLEAN: Filling in the Visibility Space
Restored Image
Restored Visibilities
Niterations = 300

---
Limits of CLEAN: Multi-Frequency Deconvolution
A baseline length is in units of wavelength, for an array which observes at multiple frequencies this means that baselines are 'shorter' for lower frequencies compared to higher frequencies.

---
Limits of CLEAN: Multi-Frequency Deconvolution
This means that the PSF resolution scales as a function of frequency.
What does it mean to make a multi-frequency image? What is the ideal size PSF if the PSF changes?

---
Limits of CLEAN: Multi-Frequency Deconvolution
Channel Imaging Method:
- make a dirty image and PSF for each frequency channel
- perform deconvolution
- average together the images to produce a single image
Pro: can account for the different PSF scale for each frequency channel
Con: reduced signal to noise by not combining all the channels leading to a shallower deconvolution
Multi-frequency Synthesis:
- make a dirty image and PSF using all channels
- perform deconvolution with an average PSF
- use an average ideal PSF to produce a restored image
Pro: maximizes signal to noise for a deeper deconvolution
Con: for wide band observations this leads to 'holes' around sources due to the average PSF subtraction

---
Limits of CLEAN: W-term Approximation
The flat-field approximation leads to w-term effects. The w-term can be seen as a phase offset → a phase offset is a change in position → the PSF is 'smeared' out as a function of distance from the phase centre.

---
Limits of CLEAN: W-term Approximation
Using Cotton-Schwab's method to do deconvolution in the visibility domain allows for w-term correction (at a computational cost).

---
Limits of CLEAN: Extended Sources
Dabbech et al 2014
CLEAN
Multi-Scale CLEAN
Compressed Sensing
MORESANE (CS)
Beam conv Image
Model
Error
Residual

---
Standard Imagers
CASA clean : full-featured imager and deconvolver included in NRAO's CASA package. (casa.nrao.edu/docs/TaskRef/clean-task.html)
lwimager : light-weight imager and deconvolver, stable but new features are not being added. (github.com/casacore/casarest)
wsclean : generic widefield imager and deconvolver. (sourceforge.net/projects/wsclean/)

---
When should you halt the deconvolution process?
i.e.
What makes a 'good' image?

---
Halting Deconvolution
Residual Image
Sky Model
Niterations = 300

---
Halting Deconvolution
Residual Image
Sky Model
Under Deconvolved → limits the resulting sky model signal
Niterations = 1000

---
Halting Deconvolution
Residual Image
Sky Model
Over Deconvolved → noise being inserted into the sky model
Niterations = 1000

---
Halting Deconvolution
Q: When should you halt the deconvolution process?
A: It is a bit ad-hoc, an interesting problem that has not been well solved.
Usually, it is based on intuition and examining the residuals and sky model for different levels of deconvolution.
Halting deconvolution is closely connected with calibration leading to a degeneracy issue.

---
Image Quality Assessment
What makes a 'good' image?
Standard metric is the dynamic range:
The ratio of the peak flux of the restored image to the noise of the image.
{\color{white} \textrm{DR} = \frac{I_{\textrm{peak}}}{\sigma_I}}

---
Limitation of Dynamic Range
An overall metric which provides no information about local variations.
In sparse images, such as interferometric images there are only a few sources and mostly noise, then artefacts (errors due to deconvolution, imaging or calibration) only occur in small, local regions. Dynamic range does not capture this information which the eye can clearly see.
Both images have nearly the same dynamic range, the one on the right has w-term artefacts

---
Limitation of Dynamic Range
The denominator of the dynamic range is ill-defined, what is the noise of the image? To calculate the noise there are a number of methods that are subjective:
1. Use the entire image
2. Use the entire residual image
3. Randomly sample the image
4. Choose a 'relatively' empty region
Resulting in different dynamic ranges figures:
1. 27.6075
2. 37.6852
3. 31.2751
4a. 38.2564 (using a corner of the image)
4b. 11.8666 (using the centre)

---
Limitation of Dynamic Range
The denominator of the dynamic range is ill-defined, what is the noise of the image? To calculate the noise there are a number of methods that are subjective:
1. Use the entire image
2. Use the entire residual image
3. Randomly sample the image
4. Choose a 'relatively' empty region
Resulting in different dynamic ranges figures:
1. 27.6075
2. 37.6852
3. 31.2751
4a. 38.2564 (using a corner of the image)
4b. 11.8666 (using the centre)

---
Image Quality Assessment
Notes:
- Look at the residual image for artefacts, the restored image is just a pretty picture.
- Dynamic range is a (weak) proxy for image quality.
- Artefacts are result of imaging, deconvolution, and calibration errors in unison.
- Image Quality Assessment is under-developed in radio interferometry
Residual Image

---
Source Finding
Clean components:
   x y flux
32 15 0.273542117836
32 15 0.218833694269
30 34 0.197043506304
32 15 0.175066955415
20 20 0.164478127268
30 34 0.157634805043
31 14 0.141743159144
20 21 0.133470733705
30 34 0.126107844035
32 20 0.124271249713
31 14 0.113394527315
29 18 0.113236796988
19 20 0.11300001035
31 16 0.109407177869
38 21 0.109218346103
21 19 0.109080307468
25 25 0.106739789818
32 9 0.106513135995
30 34 0.100886275228
Same position, different amount of flux. The final sky model is the sum of the different components at the same position
Need a way to combine 'nearby' components into a single source

---
Source Finding
Noise Image
Pixel Flux Distribution (log)

---
Source Finding
Noise w/ Sources
Pixel Flux Distribution (log)

---
Source Finding
A Gaussian using the flux mean and standard deviation results in a poor model. Better noise models can be derived from computing the mean absolute deviation or only using the negative pixel values.

---
Source Finding
Peak_Flux Pix_x Pix_y Size_x Size_y
  0.0103 153.5 255.8 7.85 9.80
  0.0102 204.4 255.6 7.88 9.81
  0.0102 306.7 204.4 8.02 9.59
  0.0102 255.8 204.5 7.90 9.88
  0.0101 204.3 306.8 8.30 9.48
  0.0100 255.0 357.4 8.30 9.47
  ...

---
Next class, optional but suggected, Thursday 1:00-3:00 in the computer lab.
Assignment 2: Implement Clark's Method, see course site for link to starting point notebook, due May 6